## Slide 1: Lane Detection
Manish Pandey,
MTech, Data Science
2022pds0024@iitjammu.ac.in

## Slide 2: Introduction
Lane Detection is a project that focuses on developing a system for accurate detection and visualization of lane lines on roads.
The project utilizes computer vision techniques and image processing algorithms to identify lane lines in real-time from input images or videos.
The primary goal of this project is to improve road safety by providing a visual representation of detected lane lines, enabling autonomous vehicles to navigate within lanes and make informed decisions.
This project has significant applications in the field of autonomous driving systems, where precise lane tracking is essential for ensuring safe and efficient navigation, contributing to the advancement of autonomous vehicle technology.

## Slide 3: Importance of Lane Detection in Autonomous Driving Systems:
Autonomous vehicles rely heavily on computer vision and sensor technologies to perceive the environment and make informed decisions.
Lane detection enables autonomous vehicles to stay within designated lanes.
Accurate lane detection improves vehicle safety, reduces accidents, and enhances overall driving experience.

## Slide 4: Lane Detection Pipeline
Gray Scale
Gaussian Smoothing
Canny Edge Detection
Region Masking
Hough Transform
Draw Lines [Mark Lane Lines with different Color]

## Slide 5: Gray scaling
Processing of single channel is faster that three channel processing.
0 to 355 0 to 255
3 channel 1 channel

## Slide 6: Gaussian Smoothing
Noise can be defined as unnecessary information in a image or video.
Reducing the noise with Gaussian filter by modify the value of the pixels to the average values of the pixels.
Smooth out the image before applying Canny edge detection so we do not detect faint edges

## Slide 7: Edge Detection
Edge detection refers to process of identifying and locating sharp discontinuities in an Image.
Different methods:
  Sobel Operator
  Laplacian of Gaussian filter
  Canny Edge Detection Algorithm
Why Canny edge detection is more optimal?
  Less sensitive to noise
  It removes streaking by using two thresholds high and low
  Offers good localization of edges and utilizes gradient of the edge to generate thin edges

## Slide 8: Canny Edge Detection
Algorithm:
Smooth image with 2D gaussian :
Compute image gradient with sobel operator:
Find gradient magnitude at each pixel:
Find gradient orientation at each pixel:
Compute Laplacian along the gradient direction at each pixel:
Find zero crossings in Laplacian to find the edge location

## Slide 9: Canny edge detection results

## Slide 10: Region Masking
We want to narrow down our analysis to a section of the image. We use masking for this purpose.
We start by creating a blank mask with the same shape as the input image.
Create a polygonal mask over the vertices.
Apply the polygonal mask to the original image resulting in a masked image over the region of interest.

## Slide 11: Masking Process

## Slide 12: Difficulties for fitting approach
Extraneous data : Which points to fit to?
Incomplete data : Only parts of the image is
visible
Noise
Solution: Hough Transform

## Slide 13: Hough Transform: Concept

## Slide 14: Multiple Line detection

## Slide 15: Better Parameterization
Issue:
  Slope of the line could be very large or very small
  More memory and computation
Solution:
  Use
  Orientation of θ is finite ,i.e. it is between 0o and 1800
  Distance ρ is finite.

## Slide 16: Better Parameterization

## Slide 17: Hough Transform
We perform Hough Transform to detect line (lane) from a video

## Slide 18: Pipeline Outputs
Gray scaling

## Slide 19: Pipeline Outputs
Gaussian Smoothing

## Slide 20: Pipeline Outputs
Canny Edge Detection

## Slide 21: Pipeline Outputs
Region Masking

## Slide 22: Pipeline Outputs
Hough Transform

## Slide 23: Final Output

## Slide 24: Input video

## Slide 25: Output video

## Slide 26: Thank You!